## Slide 1: NET-257 Lab 6 – IPv6 Addressing

## Slide 2: Why Use IPv6 Addresses?

## Slide 3: IPv6 Addresses Compression

## Slide 4: Components of IPv6 Address

## Slide 5: Components of IPv6 Address (cont’d)
Recommended prefix length /64
Global routing prefix is assigned by ISP
Notes: In IPv6, routers send Router Advertisements (RAs) to communicate various pieces of information to hosts, including the presence of the router on the network. When a device receives an RA from a router, it learns about the link-local address of the router and sets it as the default gateway for IPv6 traffic.

## Slide 6: IPv6 Addresses
Loopback address
::1
Test internal IP stack
Global unicast address
2001:0db8:85a3:0000:0000:8a2e:0370:7334
Like public IPv4 address
Link-local address
FE80::1
Same network communication
Multicast address
ff00::/8
send to multiple recipients
Unique-local address
fd00::/8
for local communications
Notes: GUA: These are globally unique, internet-routable addresses. GUAs can be configured statically or assigned dynamically.